| GNL-10003xx (Φ10mm ROUND TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-10003SRD GaAlAs Super Red Red Diffused 660 1.9 50 80 60° GNL-10003LRD GaAlAs Super Red Red Diffused 660 1.9 60 100 60° GNL-10003SRT GaAlAs Super Red Red Transparent 660 1.9 250 400 22° GNL-10003SRC GaAlAs Super Red Water Clear 660 1.9 250 400 22° GNL-10003LRC GaAlAs Super Red Water Clear 660 1.9 200 400 22° GNL-10003URC GaAlAs Super Red Water Clear 660 1.9 1000 1500 22° GNL-10003UEC AlGaInP Super Orange Water Clear 625 2.0 1500 2000 22° GNL-10003HRC AlGaInP Super Orange Water Clear 640 2.0 1000 1500 22° GNL-10003GC GaP Green Water Clear 565 2.0 40 50 22° GNL-10003UGC AlGaInP Yellow Green Water Clear 572 2.0 600 800 22° GNL-10003YC GaAsP Yellow Water Clear 585 2.0 40 50 22° GNL-10003UYC AlGaInP Super Yellow Water Clear 589 2.0 1200 1800 22° GNL-10003BC InGaN Super Blue Water Clear 470 3.5 800 1200 22° GNL-10003UBC InGaN Ultra Super Blue Water Clear 470 3.5 1000 1800 22° GNL-10003BGC InGaN Super Bluish Green Water Clear 505 3.5 3000 4000 22° GNL-10003PGC InGaN Super Pure Green Water Clear 525 3.5 3000 5000 22° GNL-10003UWC InGaN Ultra Super White Water Clear 5500K-7000K 3.5 4000 5500 22° GNL-10003VC InGaN Super Violet Water Clear 400 3.5 100 300 22° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.