| GNL-3004xx (Φ3mm ROUND TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Feature: Description: 1.Small flange without stand-off 1.The shape of this series is round 2.Long life-solid state reliability 2.General application is for indication,illumination,etc. 3.Long lead length(25.4mm) 3.These LED lamps are available with a choice of defferent 4.Versatile mounting on P.C. board or panel colors,light intensities,epoxy colors,etc. |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-3004SRD GaAlAs Super Red Red Diffused 660 1.9 70 100 60° GNL-3004SRT GaAlAs Super Red Red Transparent 660 1.9 100 200 25° GNL-3004SRC GaAlAs Super Red Water Clear 660 1.9 100 200 25° GNL-3004LRC GaAlAs Super Red Water Clear 660 1.9 200 300 25° GNL-3004URC GaAlAs Super Red Water Clear 660 1.9 400 500 25° GNL-3004UEC AlGaInP Super Orange Water Clear 625 2.0 900 1200 25° GNL-3004HRC AlGaInP Super Orange Water Clear 640 2.0 500 800 25° GNL-3004UGC AlGaInP Yellow Green Water Clear 572 2.0 350 500 25° GNL-3004UYC AlGaInP Super Yellow Water Clear 585 2.0 800 1000 25° GNL-3004BC InGaN Super Blue Water Clear 470 3.5 1000 1500 25° GNL-3004UBC InGaN Ultra Super Blue Water Clear 470 3.5 1200 2000 25° GNL-3004BGC InGaN Super Bluish Green Water Clear 505 3.5 2500 4000 25° GNL-3004PGC InGaN Super Pure Green Water Clear 525 3.5 2500 4000 25° GNL-3004WC InGaN Super White Water Clear 5500K-7500K 3.5 1500 2000 25° GNL-3004VC InGaN Ultra Super Violet Water Clear 400 3.5 150 300 25° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.