| GNL-3014xx (Φ3mm ROUND TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-3014SRD GaAlAs Super Red Red Diffused 660 1.9 70 100 60° GNL-3014SRT GaAlAs Super Red Red Transparent 660 1.9 150 200 25° GNL-3014SRC GaAlAs Super Red Water Clear 660 1.9 150 200 25° GNL-3014LRC GaAlAs Super Red Water Clear 660 1.9 200 300 25° GNL-3014URC GaAlAs Super Red Water Clear 660 1.9 500 600 25° GNL-3014UEC AlGaInP Super Orange Water Clear 625 2.0 1000 1500 25° GNL-3014HRC AlGaInP Super Orange Water Clear 640 2.0 500 800 25° GNL-3014HRT AlGaInP Super Orange Red Transparent 640 2.0 500 800 25° GNL-3014HRD AlGaInP Super Orange Red Diffused 640 2.0 150 300 60° GNL-3014UGC AlGaInP Yellow Green Water Clear 572 2.0 350 500 25° GNL-3014GC GaP Green Water Clear 565 2.0 30 40 25° GNL-3014YC GaAsP Yellow Water Clear 588 2.0 30 40 25° GNL-3014UYC AlGaInP Super Yellow Water Clear 589 2.0 800 1000 25° GNL-3014BC InGaN Super Blue Water Clear 470 3.5 1000 1500 25° GNL-3014UBC InGaN Ultra Super Blue Water Clear 470 3.5 1200 2000 25° GNL-3014BGC InGaN Super Bluish Green Water Clear 505 3.5 2500 4000 25° GNL-3014PGC InGaN Super Pure Green Water Clear 525 3.5 2500 4000 25° GNL-3014UWC InGaN Ultra Super White Water Clear 5500K-7000K 3.5 2000 3000 25° GNL-3014VC InGaN Super Violet Water Clear 400 3.5 150 300 25° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.