| GNL-8003xx (Φ8mm ROUND TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Feature: Description: 1.Small flange without stand-off 1.The shape of this series is round 2.Long life-solid state reliability 2.General application is for indication,illumination,etc. 3.Long lead length(25.4mm) 3.These LED lamps are available with a choice of defferent 4.Versatile mounting on P.C. board or panel colors,light intensities,epoxy colors,etc. |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-8003SRD GaAlAs Super Red Red Diffused 660 1.9 50 100 60° GNL-8003LRD GaAlAs Super Red Red Diffused 660 1.9 200 400 60° GNL-8003SRT GaAlAs Super Red Red Transparent 660 1.9 250 400 22° GNL-8003SRC GaAlAs Super Red Water Clear 660 1.9 250 400 22° GNL-8003LRC GaAlAs Super Red Water Clear 660 1.9 600 800 22° GNL-8003URC GaAlAs Super Red Water Clear 660 1.9 1200 1500 22° GNL-8003UEC AlGaInP Super Orange Red Water Clear 625 2.0 1500 2000 22° GNL-8003HRC AlGaInP Super Orange Red Water Clear 640 2.0 1200 1800 22° GNL-8003UEC-TL AlGaInP Super Orange Red Water Clear 625 2.0 4000 5000 22° GNL-8003UYC AlGaInP Super amber Water Clear 585 2.0 1500 2000 22° GNL-8003UYC-TL AlGaInP Super amber Water Clear 585 2.0 4000 5000 22° GNL-8003UBC InGaN Ultra Super Blue Water Clear 470 3.5 1800 3500 22° GNL-8003UBC-TL InGaN Ultra Super Blue Water Clear 470 3.5 2500 4500 22° GNL-8003UBD-TL InGaN Ultra Super Blue Blue Diffused 470 3.5 1000 1500 60° GNL-8003BC-1 InGaN Super Blue Water Clear 470 3.5 1500 2000 22° GNL-8003PGC InGaN Super Pure Green Water Clear 525 3.5 5000 9000 22° GNL-8003UWC InGaN Ultra Super White Water Clear 5500K-7000K 3.5 4000 9000 22° GNL-8003VC InGaN Super Violet Water Clear 400 3.5 100 300 22° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.